VHDL (VHSIC Hardware Description Language)
VHSIC (Very High Speed Integrated Circuits)
An acronym within an acronym
A complex language that can be simple to understand as long as you use only the part of the language you need and understand (e.g. the following notes). The examples show specific syntax and code structures that work well for synthesis and simulation. They are easy to understand so you will be able to modify the examples for you specific needs in the future.
If you deviate from the examples you may experience problems. If you google VHDL, good luck, hope you know what you are doing. Yet check at opencores.org, once you are more advanced you may have fun building systems with VHDL cores (later CSCE classes).
The examples cover a broad range of combinatorial and sequential circuits. THIS MAY BE VALUABLE FOR YOU IN THE FUTURE, KEEP THESE NOTES.

---
VHDL Language
There are three things to include in a VHDL component.
Libraries, Packages:
LIBRARY and USE packages define the language, etc.
LIBRARY ieee;
USE ieee.std_logic_1164.all;
Entity:
Defines the interface to the VHDL component. The inputs, outputs, or other types of I/O are defined here.
Architecture:
Defines the function of the component. The outputs are a function of the inputs for combinational circuits (FSM are more complex).

---
VHDL code for a function f(x1,x2,x3) = ?

---
VHDL code for the function f =  m(0, 2, 4, 5, 6)

---
The VHDL code for f =  m(2, 3, 9, 10, 11, 13)

---
VHDL code for a 7-variable function

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY fulladd IS
PORT (	Cin, x, y	: IN	STD_LOGIC ;
s, Cout	: OUT	STD_LOGIC ) ;
END fulladd ;
ARCHITECTURE LogicFunc OF fulladd IS
BEGIN
s <= x XOR y XOR Cin ;
Cout <= (x AND y) OR (Cin AND x) OR (Cin AND y) ;
END LogicFunc ;
VHDL code for a full-adder

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
USE ieee.std_logic_signed.all ;
ENTITY adder16 IS
PORT (	X, Y	: IN	STD_LOGIC_VECTOR(15 DOWNTO 0) ;
S	: OUT	STD_LOGIC_VECTOR(15 DOWNTO 0) ) ;
END adder16 ;
ARCHITECTURE Behavior OF adder16 IS
BEGIN
S <= X + Y ;
END Behavior ;
VHDL code for a 16-bit adder

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
USE ieee.std_logic_signed.all ;
ENTITY adder16 IS
PORT (	Cin	: IN	STD_LOGIC ;
X, Y	: IN	STD_LOGIC_VECTOR(15 DOWNTO 0) ;
S	: OUT	STD_LOGIC_VECTOR(15 DOWNTO 0) ;
Cout, Overflow	: OUT	STD_LOGIC ) ;
END adder16 ;
ARCHITECTURE Behavior OF adder16 IS
SIGNAL Sum : STD_LOGIC_VECTOR(16 DOWNTO 0) ;
BEGIN
Sum <= ('0' & X) + Y + Cin ;
S <= Sum(15 DOWNTO 0) ;
Cout <= Sum(16) ;
Overflow <= Sum(16) XOR X(15) XOR Y(15) XOR Sum(15) ;
END Behavior ;
A 16-bit adder with carry and overflow

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY mux2to1 IS
PORT (	w0, w1, s	: IN	STD_LOGIC ;
f	: OUT	STD_LOGIC ) ;
END mux2to1 ;
ARCHITECTURE Behavior OF mux2to1 IS
BEGIN
WITH s SELECT
f <=	w0 WHEN '0',
w1 WHEN OTHERS ;
END Behavior ;
VHDL code for a 2-to-1 multiplexer

---
s
0
s
s
s
f
1
1
0
w
w
00
0
0
0
0
w
01
w
1
0
1
f
1
w
10
w
2
1
0
2
w
11
3
w
1
1
3
(a) Graphic symbol
(b) Truth table
s
0
w
0
s
1
w
1
f
w
2
w
3
(c) Circuit
A 4-to-1 multiplexer

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY mux4to1 IS
PORT (	w0, w1, w2, w3	: IN	STD_LOGIC ;
s	: IN	STD_LOGIC_VECTOR(1 DOWNTO 0) ;
f	: OUT	STD_LOGIC ) ;
END mux4to1 ;
ARCHITECTURE Behavior OF mux4to1 IS
BEGIN
WITH s SELECT
f <= w0 WHEN "00",
w1 WHEN "01",
w2 WHEN "10",
w3 WHEN OTHERS ;
END Behavior ;
VHDL code for a 4-to-1 multiplexer

---
w
w
y
y
y
y
En
1
0
0
1
2
3
w
y
0
0
0
0
0
1
0
0
1
w
y
1
1
0
1
0
1
0
0
1
y
2
1
1
0
0
0
1
0
y
En
3
1
1
1
0
0
0
1
x
x
0
0
0
0
0
(a) Truth table
(b) Graphic symbol
w
0
y
0
w
1
y
1
y
2
y
3
En
(c) Logic circuit
A 2-to-4 decoder

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY dec2to4 IS
PORT (	w	: IN	STD_LOGIC_VECTOR(1 DOWNTO 0) ;
En	: IN	STD_LOGIC ;
y	: OUT	STD_LOGIC_VECTOR(0 TO 3) ) ;
END dec2to4 ;
ARCHITECTURE Behavior OF dec2to4 IS
SIGNAL Enw : STD_LOGIC_VECTOR(2 DOWNTO 0) ;
BEGIN
Enw <= En & w ;
WITH Enw SELECT
y <= "1000" WHEN "100",
"0100" WHEN "101",
"0010" WHEN "110",
"0001" WHEN "111",
"0000" WHEN OTHERS ;
END Behavior ;
VHDL code for a 2-to-4 binary decoder

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY mux2to1 IS
PORT (	w0, w1, s	: IN	STD_LOGIC ;
f	: OUT	STD_LOGIC ) ;
END mux2to1 ;
ARCHITECTURE Behavior OF mux2to1 IS
BEGIN
f <= w0 WHEN s = '0' ELSE w1 ;
END Behavior ;
A 2-to-1 multiplexer using a conditional signal assignment

---
w
w
w
w
y
y
z
3
2
1
0
1
0
0
0
0
0
d
d
0
0
0
0
1
0
0
1
x
0
0
1
0
1
1
x
x
0
1
1
0
1
x
x
x
1
1
1
1
Truth table for a 4-to-2 priority encoder

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY priority IS
PORT (	w	: IN	STD_LOGIC_VECTOR(3 DOWNTO 0) ;
y	: OUT	STD_LOGIC_VECTOR(1 DOWNTO 0) ;
z	: OUT	STD_LOGIC ) ;
END priority ;
ARCHITECTURE Behavior OF priority IS
BEGIN
y <=	"11" WHEN w(3) = '1' ELSE
"10" WHEN w(2) = '1' ELSE
"01" WHEN w(1) = '1' ELSE
"00" ;
z <= '0' WHEN w = "0000" ELSE '1' ;
END Behavior ;
VHDL code for a priority encoder

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY priority IS
PORT (	w	: IN	STD_LOGIC_VECTOR(3 DOWNTO 0) ;
y	: OUT	STD_LOGIC_VECTOR(1 DOWNTO 0) ;
z	: OUT	STD_LOGIC ) ;
END priority ;
ARCHITECTURE Behavior OF priority IS
BEGIN
WITH w SELECT
y <=	"00" WHEN "0001",
"01" WHEN "0010",
"01" WHEN "0011",
"10" WHEN "0100",
"10" WHEN "0101",
"10" WHEN "0110",
"10" WHEN "0111",
"11" WHEN OTHERS ;
WITH w SELECT
z <=	'0' WHEN "0000",
'1' WHEN OTHERS ;
END Behavior ;
Less efficient code for a priority encoder

---
A four-bit comparator circuit

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
USE ieee.std_logic_unsigned.all ;
ENTITY compare IS
PORT (	A, B	: IN	STD_LOGIC_VECTOR(3 DOWNTO 0) ;
AeqB, AgtB, AltB	: OUT	STD_LOGIC ) ;
END compare ;
ARCHITECTURE Behavior OF compare IS
BEGIN
AeqB <=	'1' WHEN A = B ELSE '0' ;
AgtB <= '1' WHEN A > B ELSE '0' ;
AltB <= '1' WHEN A < B ELSE '0' ;
END Behavior ;
VHDL code for a four-bit comparator

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY mux2to1 IS
PORT (	w0, w1, s	: IN	STD_LOGIC ;
f	: OUT	STD_LOGIC ) ;
END mux2to1 ;
ARCHITECTURE Behavior OF mux2to1 IS
BEGIN
PROCESS ( w0, w1, s )
BEGIN
IF s = '0' THEN
f <= w0 ;
ELSE
f <= w1 ;
END IF ;
END PROCESS ;
END Behavior ;
A 2-to-1 multiplexer specified using an if-then-else statement

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY mux2to1 IS
PORT (	w0, w1, s	: IN	STD_LOGIC ;
f	: OUT	STD_LOGIC ) ;
END mux2to1 ;
ARCHITECTURE Behavior OF mux2to1 IS
BEGIN
PROCESS ( w0, w1, s )
BEGIN
f <= w0 ;
IF s = '1' THEN
f <= w1 ;
END IF ;
END PROCESS ;
END Behavior ;
Alternative code for a 2-to-1 multiplexer

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY priority IS
PORT (	w	: IN	STD_LOGIC_VECTOR(3 DOWNTO 0) ;
y	: OUT	STD_LOGIC_VECTOR(1 DOWNTO 0) ;
z	: OUT	STD_LOGIC ) ;
END priority ;
ARCHITECTURE Behavior OF priority IS
BEGIN
PROCESS ( w )
BEGIN
IF w(3) = '1' THEN
y <= "11" ;
ELSIF w(2) = '1' THEN
y <= "10" ;
ELSIF w(1) = '1' THEN
y <= "01" ;
ELSE
y <= "00" ;
END IF ;
END PROCESS ;
z <= '0' WHEN w = "0000" ELSE '1' ;
END Behavior ;
A priority encoder specified using if-then-else

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY priority IS
PORT (	w	: IN	STD_LOGIC_VECTOR(3 DOWNTO 0) ;
y	: OUT	STD_LOGIC_VECTOR(1 DOWNTO 0) ;
z	: OUT	STD_LOGIC ) ;
END priority ;
ARCHITECTURE Behavior OF priority IS
BEGIN
PROCESS ( w )
BEGIN
y <= "00" ;
IF w(1) = '1' THEN y <= "01" ; END IF ;
IF w(2) = '1' THEN y <= "10" ; END IF ;
IF w(3) = '1' THEN y <= "11" ; END IF ;
z <= '1' ;
IF w = "0000" THEN z <= '0' ; END IF ;
END PROCESS ;
END Behavior ;
Alternative code for the priority encoder

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY compare1 IS
PORT (	A, B	: IN	STD_LOGIC ;
AeqB	: OUT	STD_LOGIC ) ;
END compare1 ;
ARCHITECTURE Behavior OF compare1 IS
BEGIN
PROCESS ( A, B )
BEGIN
AeqB <= '0' ;
IF A = B THEN
AeqB <= '1' ;
END IF ;
END PROCESS ;
END Behavior ;
Code for a one-bit equality comparator

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY mux2to1 IS
PORT (	w0, w1, s	: IN	STD_LOGIC ;
f	: OUT	STD_LOGIC ) ;
END mux2to1 ;
ARCHITECTURE Behavior OF mux2to1 IS
BEGIN
PROCESS ( w0, w1, s )
BEGIN
CASE s IS
WHEN '0' =>
f <= w0 ;
WHEN OTHERS =>
f <= w1 ;
END CASE ;
END PROCESS ;
END Behavior ;
A CASE statement that represents a 2-to-1 multiplexer

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY dec2to4 IS
PORT (	w	: IN	STD_LOGIC_VECTOR(1 DOWNTO 0) ;
En	: IN	STD_LOGIC ;
y	: OUT	STD_LOGIC_VECTOR(0 TO 3) ) ;
END dec2to4 ;
ARCHITECTURE Behavior OF dec2to4 IS
BEGIN
PROCESS ( w, En )
BEGIN
IF En = '1' THEN
CASE w IS
WHEN "00" =>	y <= "1000" ;
WHEN "01" =>	y <= "0100" ;
WHEN "10" =>	y <= "0010" ;
WHEN OTHERS =>	y <= "0001" ;
END CASE ;
ELSE
y <= "0000" ;
END IF ;
END PROCESS ;
END Behavior ;
A 2-to-4 binary decoder

---
a
a
b
w
f
b
0
c
w
1
d
w
g
2
e
e
c
w
3
f
d
g
(a) Code converter
(b) 7-segment display
c
e
g
w
w
w
w
a
b
d
f
3
2
1
0
0
0
0
0
1
1
1
1
1
1
0
0
0
0
1
0
1
1
0
0
0
0
0
0
1
0
1
1
0
1
1
0
1
0
0
1
1
1
1
1
1
0
0
1
0
1
0
0
0
1
1
0
0
1
1
0
1
0
1
1
0
1
1
0
1
1
0
1
1
0
1
0
1
1
1
1
1
1
1
1
0
1
1
1
0
0
0
0
1
1
1
1
1
1
1
1
0
0
0
1
0
0
1
1
1
1
1
0
1
1
(c) Truth table
BCD-to-7-segment display code converter

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY seg7 IS
PORT (	bcd	: IN	STD_LOGIC_VECTOR(3 DOWNTO 0) ;
leds	: OUT	STD_LOGIC_VECTOR(1 TO 7) ) ;
END seg7 ;
ARCHITECTURE Behavior OF seg7 IS
BEGIN
PROCESS ( bcd )
BEGIN
CASE bcd IS	--	abcdefg
WHEN "0000"	=> leds	<=	"1111110" ;
WHEN "0001"	=> leds	<=	"0110000" ;
WHEN "0010"	=> leds	<=	"1101101" ;
WHEN "0011"	=> leds	<=	"1111001" ;
WHEN "0100"	=> leds	<=	"0110011" ;
WHEN "0101"	=> leds	<=	"1011011" ;
WHEN "0110"	=> leds	<=	"1011111" ;
WHEN "0111"	=> leds	<=	"1110000" ;
WHEN "1000"	=> leds	<=	"1111111" ;
WHEN "1001"	=> leds	<=	"1110011" ;
WHEN OTHERS	=> leds	<=	"-------" ;
END CASE ;
END PROCESS ;
END Behavior ;
a
f
b
g
e
c
d
BCD-to-7-segment decoder

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
USE ieee.std_logic_unsigned.all ;
ENTITY alu IS
PORT (	s	: IN	STD_LOGIC_VECTOR(2 DOWNTO 0) ;
A, B	: IN	STD_LOGIC_VECTOR(3 DOWNTO 0) ;
F	: OUT	STD_LOGIC_VECTOR(3 DOWNTO 0) ) ;
END alu ;
ARCHITECTURE Behavior OF alu IS
BEGIN
PROCESS ( s, A, B )
BEGIN
CASE s IS
WHEN "000" =>
F <= "0000" ;
WHEN "001" =>
F <= B - A ;
WHEN "010" =>
F <= A - B ;
WHEN "011" =>
F <= A + B ;
WHEN "100" =>
F <= A XOR B ;
WHEN "101" =>
F <= A OR B ;
WHEN "110" =>
F <= A AND B ;
WHEN OTHERS =>
F <= "1111" ;
END CASE ;
END PROCESS ;
END Behavior ;
Code that represents the functionality of the 74381 ALU

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY reg8 IS
PORT (	D	: IN	STD_LOGIC_VECTOR(7 DOWNTO 0) ;
Resetn, Clock	: IN	STD_LOGIC ;
Q	: OUT	STD_LOGIC_VECTOR(7 DOWNTO 0) ) ;
END reg8 ;
ARCHITECTURE Behavior OF reg8 IS
BEGIN
PROCESS ( Resetn, Clock )
BEGIN
IF Resetn = '0' THEN
Q <= "00000000" ;
ELSIF Clock'EVENT AND Clock = '1' THEN
Q <= D ;
END IF ;
END PROCESS ;
END Behavior ;
Code for an eight-bit register with asynchronous clear

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY regn IS
GENERIC ( N : INTEGER := 16 ) ;
PORT (	D	: IN	STD_LOGIC_VECTOR(N-1 DOWNTO 0) ;
Resetn, Clock	: IN	STD_LOGIC ;
Q	: OUT	STD_LOGIC_VECTOR(N-1 DOWNTO 0) ) ;
END regn ;
ARCHITECTURE Behavior OF regn IS
BEGIN
PROCESS ( Resetn, Clock )
BEGIN
IF Resetn = '0' THEN
Q <= (OTHERS => '0') ;
ELSIF Clock'EVENT AND Clock = '1' THEN
Q <= D ;
END IF ;
END PROCESS ;
END Behavior ;
Code for an n-bit register with asynchronous clear

---
Parallel output
Q
Q
Q
Q
3
2
1
0
Q
Q
Q
Q
D
D
D
D
Q
Q
Q
Q
Serial
Clock
Shift/Load
input
Parallel input
Figure 7.19 A simple shift register

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY shift4 IS
PORT (	R	: IN	STD_LOGIC_VECTOR(3 DOWNTO 0) ;
Clock	: IN	STD_LOGIC ;
L, w	: IN	STD_LOGIC ;
Q	: BUFFER	STD_LOGIC_VECTOR(3 DOWNTO 0) ) ;
END shift4 ;
ARCHITECTURE Behavior OF shift4 IS
BEGIN
PROCESS
BEGIN
WAIT UNTIL Clock'EVENT AND Clock = '1' ;
IF L = '1' THEN
Q <= R ;
ELSE
Q(0) <= Q(1) ;
Q(1) <= Q(2);
Q(2) <= Q(3) ;
Q(3) <= w ;
END IF ;
END PROCESS ;
END Behavior ;
Code for a shift register

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY shift4 IS
PORT (	R	: IN	STD_LOGIC_VECTOR(3 DOWNTO 0) ;
Clock	: IN	STD_LOGIC ;
L, w	: IN	STD_LOGIC ;
Q	: BUFFER	STD_LOGIC_VECTOR(3 DOWNTO 0) ) ;
END shift4 ;
ARCHITECTURE Behavior OF shift4 IS
BEGIN
PROCESS
BEGIN
WAIT UNTIL Clock'EVENT AND Clock = '1' ;
IF L = '1' THEN
Q <= R ;
ELSE
Q(3) <= w ;
Q(2) <= Q(3) ;
Q(1) <= Q(2);
Q(0) <= Q(1) ;
END IF ;
END PROCESS ;
END Behavior ;
Code that reverses the ordering of statements

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
USE ieee.std_logic_unsigned.all ;
ENTITY upcount IS
PORT (	Clock, Resetn, E	: IN	STD_LOGIC ;
Q	: OUT	STD_LOGIC_VECTOR (3 DOWNTO 0)) ;
END upcount ;
ARCHITECTURE Behavior OF upcount IS
SIGNAL Count : STD_LOGIC_VECTOR (3 DOWNTO 0) ;
BEGIN
PROCESS ( Clock, Resetn )
BEGIN
IF Resetn = '0' THEN
Count <= "0000" ;
ELSIF (Clock'EVENT AND Clock = '1') THEN
IF E = '1' THEN
Count <= Count + 1 ;
ELSE
Count <= Count ;
END IF ;
END IF ;
END PROCESS ;
Q <= Count ;
END Behavior ;
Code for a four-bit up-counter

---
Reset
w
=
1


A
z
=
0
B
z
=
0
w
=
0
w
=
0
w
=
1
w
=
0

C
z
=
1
w
=
1
State diagram of a simple sequential circuit (Moore Machine)

---
USE ieee.std_logic_1164.all ;
ENTITY simple IS
PORT (	Clock, Resetn, w	: IN	STD_LOGIC ;
z	: OUT	STD_LOGIC ) ;
END simple ;
ARCHITECTURE Behavior OF simple IS
TYPE State_type IS (A, B, C) ;
SIGNAL y : State_type ;
BEGIN
PROCESS ( Resetn, Clock )
BEGIN
IF Resetn = '0' THEN
y <= A ;
ELSIF (Clock'EVENT AND Clock = '1') THEN
con’t ...
VHDL code for a simple FSM

---
CASE y IS
WHEN A =>
IF w = '0' THEN
y <= A ;
ELSE
y <= B ;
END IF ;
WHEN B =>
IF w = '0' THEN
y <= A ;
ELSE
y <= C ;
END IF ;
WHEN C =>
IF w = '0' THEN
y <= A ;
ELSE
y <= C ;
END IF ;
END CASE ;
END IF ;
END PROCESS ;
z <= '1' WHEN y = C ELSE '0' ;
END Behavior ;
VHDL code for a simple FSM (con’t)

---
(a) Timing simulation results
(b) Magnified simulation results, showing timing details
Simulation results

---
(ENTITY declaration not shown)
ARCHITECTURE Behavior OF simple IS
TYPE State_type IS (A, B, C) ;
SIGNAL y_present, y_next : State_type ;
BEGIN
PROCESS ( w, y_present )
BEGIN
CASE y_present IS
WHEN A =>
IF w = '0' THEN
y_next <= A ;
ELSE
y_next <= B ;
END IF ;
WHEN B =>
IF w = '0' THEN
y_next <= A ;
ELSE
y_next <= C ;
END IF ;
Alternative style of code for an FSM

---
WHEN C =>
IF w = '0' THEN
y_next <= A ;
ELSE
y_next <= C ;
END IF ;
END CASE ;
END PROCESS ;
PROCESS (Clock, Resetn)
BEGIN
IF Resetn = '0' THEN
y_present <= A ;
ELSIF (Clock'EVENT AND Clock = '1') THEN
y_present <= y_next ;
END IF ;
END PROCESS ;
z <= '1' WHEN y_present = C ELSE '0' ;
END Behavior ;
Alternative style of code for an FSM (con’t)

---
Reset

w
=
1
z
=
0


w
=
0
z
=
0
w
=
1
z
=
1
A
B

w
=
0
z
=
0
Mealy FSM State diagram

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY mealy IS
PORT (	Clock, Resetn, w	: IN	STD_LOGIC ;
z	: OUT	STD_LOGIC ) ;
END mealy ;
ARCHITECTURE Behavior OF mealy IS
TYPE State_type IS (A, B) ;
SIGNAL y : State_type ;
BEGIN
PROCESS ( Resetn, Clock )
BEGIN
IF Resetn = '0' THEN
y <= A ;
ELSIF (Clock'EVENT AND Clock = '1') THEN
CASE y IS
WHEN A =>
IF w = '0' THEN y <= A ;
ELSE y <= B ;
END IF ;
… con’t
Reset

w
=
1
z
=
0

w
=
1
z
=
1
A
B

w
=
0
z
=
0

w
=
0
z
=
0
VHDL code for a Mealy machine

---
WHEN B =>
IF w = '0' THEN y <= A ;
ELSE y <= B ;
END IF ;
END CASE ;
END IF ;
END PROCESS ;
PROCESS ( y, w )
BEGIN
CASE y IS
WHEN A =>
z <= '0' ;
WHEN B =>
z <= w ;
END CASE ;
END PROCESS ;
END Behavior ;
Reset

w
=
1
z
=
0


w
=
0
z
=
0
w
=
1
z
=
1
A
B

w
=
0
z
=
0
VHDL code for a Mealy machine (con’t)

---
Reset

w
=
1
z
=
0


w
=
0
z
=
0
w
=
1
z
=
1
A
B

w
=
0
z
=
0
Simulation results for the Mealy machine

---
A
a
Shift register
s
Adder
Shift register
FSM
Shift register
b
Sum
A
B
=
+
B
Clock
Block diagram of a serial adder

---
State diagram for the serial adder

---
s
Next state
Output
Present
state
ab
=00
01
10
11
00
01
10
11
G
G
G
G
H
0
1
1
0
H
G
H
H
H
1
0
0
1
State table for the serial adder

---
Next state
Output
Present
state
ab
=00
01
10
11
00
01
10
11
y
Y
s
0
0
0
0
1
0
1
1
0
1
0
1
1
1
1
0
0
1
State-assigned table for the serial adder

---
s
a
Full
b
adder
Y
y
Q
D
carry-out
Clock
Q
Reset
Circuit for the adder FSM

---
Reset
11
01


G
s
=
0
H
s
=
0
00
0
0
10
00
01
01
00
11
11
10
10
01


G
s
=
1
H
s
=
1
11
1
1
10
00
State diagram for the Moore-type serial adder FSM

---
Nextstate
Present
Output
state
ab
=00
01
10
11
s
G
G
G
G
H
0
0
0
1
1
0
G
G
G
G
H
1
1
0
1
1
0
H
G
H
H
H
0
0
1
0
0
1
H
G
H
H
H
1
1
1
0
0
1
State table for the Moore-type serial adder FSM

---
Nextstate
Present
Output
ab
state
=00
01
10
11
y
y
s
2
1
Y
Y
2
1
00
0
0
01
0
1
10
0
01
0
0
01
0
1
10
1
10
0
1
10
1
0
11
0
11
0
1
10
1
0
11
1
State-assigned table for the Moore-type serial adder FSM

---
y
Y
Sum bit
1
1
a
s
Q
D
Full
b
adder
Carry-out
Q
Y
y
2
2
Q
D
Clock
Q
Reset
Circuit for the Moore-type serial adder FSM

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
-- left-to-right shift register with parallel load and enable
ENTITY shiftrne IS
GENERIC ( N : INTEGER := 4 ) ;
PORT (	R	: IN	STD_LOGIC_VECTOR(N-1 DOWNTO 0) ;
L, E, w	: IN	STD_LOGIC ;
Clock	: IN	STD_LOGIC ;
Q	: BUFFER	STD_LOGIC_VECTOR(N-1 DOWNTO 0) ) ;
END shiftrne ;
ARCHITECTURE Behavior OF shiftrne IS
BEGIN
PROCESS
BEGIN
… con’t
Code for a left-to-right shift register with an enable input

---
WAIT UNTIL Clock'EVENT AND Clock = '1' ;
IF E = '1' THEN
IF L = '1' THEN
Q <= R ;
ELSE
Genbits: FOR i IN 0 TO N-2 LOOP
Q(i) <= Q(i+1) ;
END LOOP ;
Q(N-1) <= w ;
END IF ;
END IF ;
END PROCESS ;
END Behavior ;
Code for a left-to-right shift register with an enable input (con’t)

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY serial IS
GENERIC ( length : INTEGER := 8 ) ;
PORT (	Clock	: IN	STD_LOGIC ;
Reset	: IN	STD_LOGIC ;
A, B	: IN	STD_LOGIC_VECTOR(length-1 DOWNTO 0) ;
Sum	: BUFFER	STD_LOGIC_VECTOR(length-1 DOWNTO 0) );
END serial ;
ARCHITECTURE Behavior OF serial IS
COMPONENT shiftrne
GENERIC ( N : INTEGER := 4 ) ;
PORT (	R	: IN	STD_LOGIC_VECTOR(N-1 DOWNTO 0) ;
L, E, w	: IN	STD_LOGIC ;
Clock	: IN	STD_LOGIC ;
Q	: BUFFER	STD_LOGIC_VECTOR(N-1 DOWNTO 0) ) ;
END COMPONENT ;
SIGNAL QA, QB, Null_in : STD_LOGIC_VECTOR(length-1 DOWNTO 0) ;
SIGNAL s, Low, High, Run : STD_LOGIC ;
SIGNAL Count : INTEGER RANGE 0 TO length ;
TYPE State_type IS (G, H) ;
SIGNAL y : State_type ;
… con’t
VHDL code for the serial adder

---
BEGIN
Low <= '0' ; High <= '1' ;
ShiftA: shiftrne	GENERIC MAP (N => length)
PORT MAP ( A, Reset, High, Low, Clock, QA ) ;
ShiftB: shiftrne GENERIC MAP (N => length)
PORT MAP ( B, Reset, High, Low, Clock, QB ) ;
AdderFSM: PROCESS ( Reset, Clock )
BEGIN
IF Reset = '1' THEN
y <= G ;
ELSIF Clock'EVENT AND Clock = '1' THEN
CASE y IS
WHEN G =>
IF QA(0) = '1' AND QB(0) = '1' THEN y <= H ;
ELSE y <= G ;
END IF ;
WHEN H =>
IF QA(0) = '0' AND QB(0) = '0' THEN y <= G ;
ELSE y <= H ;
END IF ;
END CASE ;
END IF ;
END PROCESS AdderFSM ;
… con’t
VHDL code for the serial adder (con’t)

---
WITH y SELECT
s <=	QA(0) XOR QB(0) WHEN G,
NOT ( QA(0) XOR QB(0) ) WHEN H ;
Null_in <= (OTHERS => '0') ;
ShiftSum: shiftrne GENERIC MAP ( N => length )
PORT MAP ( Null_in, Reset, Run, s, Clock, Sum ) ;
Stop: PROCESS
BEGIN
WAIT UNTIL (Clock'EVENT AND Clock = '1') ;
IF Reset = '1' THEN
Count <= length ;
ELSIF Run = '1' THEN
Count <= Count -1 ;
END IF ;
END PROCESS ;
Run <= '0' WHEN Count = 0 ELSE '1' ; -- stops counter and ShiftSum
END Behavior ;
VHDL code for the serial adder (con’t)

---
1
0
0
0
a
a
D
D
D
D
7
0
3
2
1
0
L
Counter
E
L
w
0
Q
Q
Q
Q
3
2
1
0
1
E
Adder
b
b
FSM
7
0
Run
L
0
0
w
0
1
E
L
w
E
Clock
Reset
Sum
Sum
7
0
Synthesized serial adder

---
Simulation results for the synthesized serial adder

---
Reset
w
=
1


A
z
=
0
B
z
=
0
w
=
0
w
=
0
w
=
1
w
=
0

C
z
=
1
w
=
1
State diagram of a simple sequential circuit (Moore Machine)

---
USE ieee.std_logic_1164.all ;
ENTITY simple IS
PORT (	Clock, Resetn, w	: IN	STD_LOGIC ;
z	: OUT	STD_LOGIC ) ;
END simple ;
ARCHITECTURE Behavior OF simple IS
TYPE State_type IS (A, B, C) ;
SIGNAL y : State_type ;
BEGIN
PROCESS ( Resetn, Clock )
BEGIN
IF Resetn = '0' THEN
y <= A ;
ELSIF (Clock'EVENT AND Clock = '1') THEN
con’t ...
VHDL code for a simple FSM

---
CASE y IS
WHEN A =>
IF w = '0' THEN
y <= A ;
ELSE
y <= B ;
END IF ;
WHEN B =>
IF w = '0' THEN
y <= A ;
ELSE
y <= C ;
END IF ;
WHEN C =>
IF w = '0' THEN
y <= A ;
ELSE
y <= C ;
END IF ;
END CASE ;
END IF ;
END PROCESS ;
z <= '1' WHEN y = C ELSE '0' ;
END Behavior ;
VHDL code for a simple FSM (con’t)

---
(a) Timing simulation results
(b) Magnified simulation results, showing timing details
Simulation results

---
(ENTITY declaration not shown)
ARCHITECTURE Behavior OF simple IS
TYPE State_type IS (A, B, C) ;
SIGNAL y_present, y_next : State_type ;
BEGIN
PROCESS ( w, y_present )
BEGIN
CASE y_present IS
WHEN A =>
IF w = '0' THEN
y_next <= A ;
ELSE
y_next <= B ;
END IF ;
WHEN B =>
IF w = '0' THEN
y_next <= A ;
ELSE
y_next <= C ;
END IF ;
Alternative style of code for an FSM

---
WHEN C =>
IF w = '0' THEN
y_next <= A ;
ELSE
y_next <= C ;
END IF ;
END CASE ;
END PROCESS ;
PROCESS (Clock, Resetn)
BEGIN
IF Resetn = '0' THEN
y_present <= A ;
ELSIF (Clock'EVENT AND Clock = '1') THEN
y_present <= y_next ;
END IF ;
END PROCESS ;
z <= '1' WHEN y_present = C ELSE '0' ;
END Behavior ;
Alternative style of code for an FSM (con’t)

---
Reset

w
=
1
z
=
0


w
=
0
z
=
0
w
=
1
z
=
1
A
B

w
=
0
z
=
0
Mealy FSM State diagram

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY mealy IS
PORT (	Clock, Resetn, w	: IN	STD_LOGIC ;
z	: OUT	STD_LOGIC ) ;
END mealy ;
ARCHITECTURE Behavior OF mealy IS
TYPE State_type IS (A, B) ;
SIGNAL y : State_type ;
BEGIN
PROCESS ( Resetn, Clock )
BEGIN
IF Resetn = '0' THEN
y <= A ;
ELSIF (Clock'EVENT AND Clock = '1') THEN
CASE y IS
WHEN A =>
IF w = '0' THEN y <= A ;
ELSE y <= B ;
END IF ;
… con’t
Reset

w
=
1
z
=
0

w
=
1
z
=
1
A
B

w
=
0
z
=
0

w
=
0
z
=
0
VHDL code for a Mealy machine

---
WHEN B =>
IF w = '0' THEN y <= A ;
ELSE y <= B ;
END IF ;
END CASE ;
END IF ;
END PROCESS ;
PROCESS ( y, w )
BEGIN
CASE y IS
WHEN A =>
z <= '0' ;
WHEN B =>
z <= w ;
END CASE ;
END PROCESS ;
END Behavior ;
Reset

w
=
1
z
=
0


w
=
0
z
=
0
w
=
1
z
=
1
A
B

w
=
0
z
=
0
VHDL code for a Mealy machine (con’t)

---
Reset

w
=
1
z
=
0


w
=
0
z
=
0
w
=
1
z
=
1
A
B

w
=
0
z
=
0
Simulation results for the Mealy machine

---
A
a
Shift register
s
Adder
Shift register
FSM
Shift register
b
Sum
A
B
=
+
B
Clock
Block diagram of a serial adder

---
State diagram for the serial adder

---
s
Next state
Output
Present
state
ab
=00
01
10
11
00
01
10
11
G
G
G
G
H
0
1
1
0
H
G
H
H
H
1
0
0
1
State table for the serial adder

---
Next state
Output
Present
state
ab
=00
01
10
11
00
01
10
11
y
Y
s
0
0
0
0
1
0
1
1
0
1
0
1
1
1
1
0
0
1
State-assigned table for the serial adder

---
s
a
Full
b
adder
Y
y
Q
D
carry-out
Clock
Q
Reset
Circuit for the adder FSM

---
Reset
11
01


G
s
=
0
H
s
=
0
00
0
0
10
00
01
01
00
11
11
10
10
01


G
s
=
1
H
s
=
1
11
1
1
10
00
State diagram for the Moore-type serial adder FSM

---
Nextstate
Present
Output
state
ab
=00
01
10
11
s
G
G
G
G
H
0
0
0
1
1
0
G
G
G
G
H
1
1
0
1
1
0
H
G
H
H
H
0
0
1
0
0
1
H
G
H
H
H
1
1
1
0
0
1
State table for the Moore-type serial adder FSM

---
Nextstate
Present
Output
ab
state
=00
01
10
11
y
y
s
2
1
Y
Y
2
1
00
0
0
01
0
1
10
0
01
0
0
01
0
1
10
1
10
0
1
10
1
0
11
0
11
0
1
10
1
0
11
1
State-assigned table for the Moore-type serial adder FSM

---
y
Y
Sum bit
1
1
a
s
Q
D
Full
b
adder
Carry-out
Q
Y
y
2
2
Q
D
Clock
Q
Reset
Circuit for the Moore-type serial adder FSM

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
-- left-to-right shift register with parallel load and enable
ENTITY shiftrne IS
GENERIC ( N : INTEGER := 4 ) ;
PORT (	R	: IN	STD_LOGIC_VECTOR(N-1 DOWNTO 0) ;
L, E, w	: IN	STD_LOGIC ;
Clock	: IN	STD_LOGIC ;
Q	: BUFFER	STD_LOGIC_VECTOR(N-1 DOWNTO 0) ) ;
END shiftrne ;
ARCHITECTURE Behavior OF shiftrne IS
BEGIN
PROCESS
BEGIN
… con’t
Code for a left-to-right shift register with an enable input

---
WAIT UNTIL Clock'EVENT AND Clock = '1' ;
IF E = '1' THEN
IF L = '1' THEN
Q <= R ;
ELSE
Genbits: FOR i IN 0 TO N-2 LOOP
Q(i) <= Q(i+1) ;
END LOOP ;
Q(N-1) <= w ;
END IF ;
END IF ;
END PROCESS ;
END Behavior ;
Code for a left-to-right shift register with an enable input (con’t)

---
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY serial IS
GENERIC ( length : INTEGER := 8 ) ;
PORT (	Clock	: IN	STD_LOGIC ;
Reset	: IN	STD_LOGIC ;
A, B	: IN	STD_LOGIC_VECTOR(length-1 DOWNTO 0) ;
Sum	: BUFFER	STD_LOGIC_VECTOR(length-1 DOWNTO 0) );
END serial ;
ARCHITECTURE Behavior OF serial IS
COMPONENT shiftrne
GENERIC ( N : INTEGER := 4 ) ;
PORT (	R	: IN	STD_LOGIC_VECTOR(N-1 DOWNTO 0) ;
L, E, w	: IN	STD_LOGIC ;
Clock	: IN	STD_LOGIC ;
Q	: BUFFER	STD_LOGIC_VECTOR(N-1 DOWNTO 0) ) ;
END COMPONENT ;
SIGNAL QA, QB, Null_in : STD_LOGIC_VECTOR(length-1 DOWNTO 0) ;
SIGNAL s, Low, High, Run : STD_LOGIC ;
SIGNAL Count : INTEGER RANGE 0 TO length ;
TYPE State_type IS (G, H) ;
SIGNAL y : State_type ;
… con’t
VHDL code for the serial adder

---
BEGIN
Low <= '0' ; High <= '1' ;
ShiftA: shiftrne	GENERIC MAP (N => length)
PORT MAP ( A, Reset, High, Low, Clock, QA ) ;
ShiftB: shiftrne GENERIC MAP (N => length)
PORT MAP ( B, Reset, High, Low, Clock, QB ) ;
AdderFSM: PROCESS ( Reset, Clock )
BEGIN
IF Reset = '1' THEN
y <= G ;
ELSIF Clock'EVENT AND Clock = '1' THEN
CASE y IS
WHEN G =>
IF QA(0) = '1' AND QB(0) = '1' THEN y <= H ;
ELSE y <= G ;
END IF ;
WHEN H =>
IF QA(0) = '0' AND QB(0) = '0' THEN y <= G ;
ELSE y <= H ;
END IF ;
END CASE ;
END IF ;
END PROCESS AdderFSM ;
… con’t
VHDL code for the serial adder (con’t)

---
WITH y SELECT
s <=	QA(0) XOR QB(0) WHEN G,
NOT ( QA(0) XOR QB(0) ) WHEN H ;
Null_in <= (OTHERS => '0') ;
ShiftSum: shiftrne GENERIC MAP ( N => length )
PORT MAP ( Null_in, Reset, Run, s, Clock, Sum ) ;
Stop: PROCESS
BEGIN
WAIT UNTIL (Clock'EVENT AND Clock = '1') ;
IF Reset = '1' THEN
Count <= length ;
ELSIF Run = '1' THEN
Count <= Count -1 ;
END IF ;
END PROCESS ;
Run <= '0' WHEN Count = 0 ELSE '1' ; -- stops counter and ShiftSum
END Behavior ;
VHDL code for the serial adder (con’t)

---
1
0
0
0
a
a
D
D
D
D
7
0
3
2
1
0
L
Counter
E
L
w
0
Q
Q
Q
Q
3
2
1
0
1
E
Adder
b
b
FSM
7
0
Run
L
0
0
w
0
1
E
L
w
E
Clock
Reset
Sum
Sum
7
0
Synthesized serial adder

---
Simulation results for the synthesized serial adder